IMPLEMENTATION OF LOCAL COMPETITION

CRTC INDUSTRY STEERING COMMITTEE

REPORT to the CRTC

by

BUILDING ACCESS AND INSIDE WIRING WG

Consensus Report

TITLE:	DEMARCATION POINT LOCATION FOR PROVISIONING OF PAY TELEPHONE BASIC ACCESS LINE SERVICE – Manitoba Telecom Services (MTS)

DATE:		2 March 2000

IMPLEMENTATION OF LOCAL COMPETITION

REPORT

Date Submitted:  2 March 2000

SUB-GROUP: Building Access & Inside Wiring

REPORT #: 016						File ID: BIRE016.DOC

REPORT TITLE: 	DEMARCATION POINT LOCATION FOR PROVISIONING OF PAY TELEPHONE BASIC ACCESS LINE SERVICE – Manitoba Telecom Services (MTS)

OUTCOME: Consensus

## RELATED TASK(s) #: N/A

BACKGROUND:

DEMARCATION

MTS's contribution, BICO036 proposed an interim demarcation policy respecting competitive payphone access lines (PALs), pending the Commission's decision on demarcation in multi-tenant buildings.  In Telecom Decision CRTC 99-10, Location of Demarcation Point for Inside Wire in Multi-Dwelling Units (MDUs) and Associated Issues, the CRTC made the following determination on competitive payphone demarcation:

". . . The Commission therefore considers that the demarcation point for PALs terminating in MDUs should be in the main terminal room, as it is for local loops. . . ."

On 14 January 2000 MTS issued a revised contribution – BICO036a to reflect the Commission’s determinations in Decision 99-10.

BICO036a was reviewed at the January 25, 2000 meeting of the BA & IW WG.  All parties at the meeting agreed to the proposed demarcation points provided in this contribution

REUSE OF INSIDE WIRE

BICO036a provides a list of MTS locations of service provider demarcation points for the provisioning of competitive payphone access lines (PAL). The service provider demarcation point is defined as the point where the local loop ( which is the responsibility of the ILEC) ends and the inside wire (which is the responsibility of the customer) begins.

MTS access technicians are responsible for removing the existing payphones and associated furniture on all “out” orders. Generally, the inside service wire previously connected to the payphone is not be removed. A proper demarcation point device is also installed at the service provider demarcation point and the circuit is tagged.

The new Competitive Payphone Telephone Service Provider (CPTSP) have asked for the position of incumbent payphone service providers regarding the reuse of the inside service wire left in place by incumbents to connect their own payphones.

CONCLUSIONS:

Location of the Demarcation Point for provisioning Competitive Payphone Access Lines

Following is a list of MTS's Payphone Access Line demarcation points based on the following 3 criteria:

- Type of building;

- Who controls the in-building facilities; and

Where MTS's entrance facilities terminate.

Manitoba Telecom Services Inc. (MTS)

Payphone Access Line Service Provider Demarcation Policy

For all Payphone Access Lines provided by MTS in MTS’s Operating Territory

| Building Type | Who Controls the In-building Facilities | Termination of Entrance Facilities | Service Provider Demarcation Point |
| --- | --- | --- | --- |
| Multi-tenant - Shopping Mall (payphone in a public location) | MTS | Inside the building | Riser closest to the payphone location (closet/panel) |
|  | Property Owner | Inside the building | MTR/Underground Terminal |
|  |  | External (Rear Wall/Pole) | Outside Rear Wall |
| Multi-tenant - Shopping Mall (payphone in a store/restaurant) | MTS | Inside the building | Within 15m of first point of entry into store/restaurant |
|  | Property Owner | Inside the building | MTR/Underground Terminal |
|  |  | External (Rear Wall/Pole) | Outside Rear Wall |
| Hotels / Congress Centers / Hospitals / Universities | MTS | Inside the building | Riser closest to the payphone location (closet/panel) |
|  | Property Owner | Inside the building | MTR/Underground Terminal |
| Airports | MTS | Inside the building | Riser closest to the payphone location (closet/panel) |
|  | Property Owner | Inside the building | MTR/Underground Terminal |
| Schools | MTS | Inside the building | Riser closest to the payphone location (closet/panel) |
|  | Property Owner | Inside the building | MTR/Underground Terminal |
|  |  | External (Rear Wall/Pole) | Outside Rear Wall |
| Bus Terminal | MTS | Inside the building | Riser closest to the payphone location (closet/panel) |
|  | Property Owner | Inside the building | MTR/Underground Terminal |
|  |  | External (Rear Wall/Pole) | Outside Rear Wall |

Manitoba Telecom Services Inc. (MTS)

Payphone Access Line Service Provider Demarcation Policy

For all Payphone Access Lines provided by MTS in MTS Operating Territory

| Building Type | Who Controls the In-building Facilities | Termination of Entrance Facilities | Service Provider Demarcation Point |
| --- | --- | --- | --- |
| Single Line Business (e.g. Restaurants) | MTS or Property Owner | Inside the building | MTR/Underground Terminal |
|  |  | External (Rear Wall/Pole) | Outside Rear Wall |
| Phone Booths Outdoors | N/A (Aerial facilities available) | External (Rear Wall/Pole) | Mast on phone booth |
|  | N/A (Aerial facilities not available) | -- | Pre-visit required with demarcation to be determined on a case by case basis (see footnote 2) |
| Special Events Outdoors (where MTS uses existing mobile payphone trailers) | N/A | -- | Pre-visit required with demarcation to be determined on a case by case basis (see footnote 2) |

## Reuse of Inside Wire

As discussed above, the inside wire previously connected to the payphone is generally not removed. However, the technicians, after the removal of the payphones will arrange the payphone location and the wire to ensure that it is completely safe and secure for the public.

MTS has no objection to the reuse of the inside service wire left in place by MTS by the CPTSPs to connect its own payphones, under the following conditions:

1) MTS does not guarantee that inside service wire will be left in place in all cases;

2) MTS does not guarantee that inside service wire left in place will be adequate for service before or at the moment the CPTSPs wish to use it;

3) MTS will not, in any case, propose or suggest to install or repair inside wire beyond the service provider demarcation point location whether by their own technicians or their representatives;

4) MTS’s responsibility on a PAL line is to ensure dial tone at the service provider demarcation point;

5) MTS will not be responsible of any damage caused by the usage by the CPTSP of the inside service wire left in place by MTS.

# Footnotes

MTR = Main Terminal Room

For outdoor locations, where there is neither aerial nor buried drop wire in place, demarcation will be determined on a case by case basis and charges may apply.  Written authorization from the appropriate authority will be required.